## Slide 1
Converting load data to design targets
SAE FD&E Fall Meeting
Dan Lingenfelser
11 October 2017
Accurate simulations require accurate inputs
What is the greatest source of uncertainty in life prediction?

## Slide 2
Distribution/Uncertainty of Load Histories
Geometry variation & uncertainty
Future Life Prediction Model
Stress/strain curve
UTS/ductility
Initiation properties
Da/DN properties
Toughness
Variability/Uncertainty
Material Properties
Probabilistic Fatigue Analysis
Uncertainty analysis
Business Risk Analysis
Commercial Factors
Objective of Analysis is Decision, Better Product, etc
50%
99%
% Failure
Cumulative Usage Indicator
(Hours, Miles, etc)

## Slide 3: FDE scope of interest and total life focus
Understand Distribution of Stresses/Strains
Includes processing induced stresses & geometry
Understand Material Characteristics
Includes fatigue, stress-strain, microstructure, density
Measure & Understand Operational Loads
Life Estimates, Trends & Key Factors Influencing Life
Fatigue Modeling to Convert Information into Life Estimates
Accelerated Testing with Correlation & Confidence
Comparison between Simulation Modeling & Test Results

## Slide 4: References for load profile analysis
Socie, D. F., and Pompetzki, M.A., “Modeling Variability in Service Loading Spectra,” Probabilistic Aspects of Life Prediction, ASTM STP 1450, W.S. Johnson and B.M. Hillberry, Eds., ASTM International, West Conshohocken, PA, 2003
  Describes a methodology for statistically extrapolating a single measured service loading history to the expected long term service usage spectra.
Andrew Halfpenny and Mark Pompetzki , “Proving Ground Optimization and Damage Correlation with Customer Usage”, SAE paper 2011-01-0484, 2011
  Proving ground damage is correlated with target customer usage
Guo, H. and Dronzkowski, D., "On Determining Road Profiles for Vehicle Level Reliability Growth Testing," SAETechnical Paper 2016-01-0272, 2016
  Customer survey data is used to identify an appropriate road profile by defining a route that represents the Xth percentile customer

## Slide 5: Example from reference 3
Table 4. Observations of the Made Up Example
Table 5. 95th Percentile and Normalized 95th Percentile for the Made Up Example
Figure 2. Simplex plot for 3 variables

## Slide 6: Potential FDE project
How do we develop design loads?
  Not as simple as go to job site and take data
  Usually involves some statistical analysis of data to establish percentile
  Many successful methods in use
  No single right answer – multiple alternatives
How should we develop design loads?
Multiple sources of load data to consider
  Measured customer loads
  Proving grounds loads
  Simulations

## Slide 7: Proposal
Create task group
Survey to gather list of methods used
  Including literature search
Evaluate and document methods
  Describe method and list pros/cons, etc.
Make recommendations
Result could be report outlining and comparing methods
  Complete in 12 months

## Slide 8
Volunteers?
Project will go where group takes it
Or it will not go